## Slide 1
Dr Rebecca (Becky) Bell and Raul Adriaensen
2nd floor, office 2.37a
rebecca.bell@imperial.ac.uk
Seismic reflection data
Lecture 2

## Slide 2: Module outline
Day 1 morning- Introduction to seismic data
Lecture 1: Physical principles
Lecture 2: Data acquisition
Lecture 3: Key data processing steps
Day 1 afternoon- Exercises
Exercise 1: Synthetic seismic models
Exercise 2: Viewing “raw” data gathers and conducting NMO corrections and velocity analysis
We will discuss the “solutions” to the exercises during the afternoon sessions (and these will be recorded)

## Slide 3: Lecture outline
Objectives of lecture 2:
Learn how seismic reflection surveys are conducted
and what equipment is used
i) Experiment design
ii) Sources and receivers
iii) The ideal wavelet

## Slide 4: Zero-offset survey
The easiest way to create a SEISMIC SECTION is to conduct a zero-offset survey:
The problem is, reflection coefficients are very small, so the reflections have low amplitude
Shot
Record
Rc = +’ve
This is what you
will effectively be
doing in exercise 1

## Slide 5: Zero-offset survey
The easiest way to create a SEISMIC SECTION is to conduct a zero-offset survey:
The problem is, reflection coefficients are very small, so the reflections have low amplitude
Shot
Record
Rc = +’ve

## Slide 6: 2D Survey geometry
We arrange traces into Common-
Mid-Points (CMPS; also
sometimes called Common
Depth Points, CDPs)- LECTURE 3
This allows us to improve
our signal to noise ratio (S/N)
by stacking traces with the
same CMPs.
This is a key, fundamental idea
behind the seismic reflection
technique
We design seismic surveys so
points in the sub-surface are sampled
more than once

## Slide 7: 2D Survey geometry
The “roll-along” method is an efficient way to acquire seismic reflection
data that is very amenable to stacking:

## Slide 8: 2D Survey geometry
The “roll-along” method is an efficient way to acquire seismic reflection
data that is very amenable to stacking:

## Slide 9: 2D Survey geometry
The “roll-along” method is an efficient way to acquire seismic reflection data that is very amenable to stacking:
4 fold
CMP/CDP profiling

## Slide 10: 2D Survey geometry
The “roll-along” method is an efficient way to acquire seismic reflection data that is very amenable to stacking:
4 fold
CMP/CDP profiling
Common depth point profiling

## Slide 11: Survey design
Wang,
pers comm

## Slide 12: 3D Survey geometry
In 3D, a Common Depth Point is sampled by
ray paths from an areal (rather than linear)
distribution of sources and receivers

## Slide 13: Sources: what we do not do…
https://www.youtube.com/watch?v=UiNhC9K7KjQ

## Slide 14: Seismic Sources
LAND
MARINE
Kearey, Brooks & Hill.
An introduction to
Geophysical Exploration
Consider the depth to your target of interest
and the resolution you need

## Slide 15
V = fλ
You would like to image marine shallow sedimentary
layers <0.5 m thick, in an area with P-wave velocity of 2.4km/s
What source will you use?

## Slide 16: Land sources
Dynamite
Vibroseis
Advantages
Disadvantages
  Wide frequency range, High energy Choice of shot depth, High data quality, All terrain
  Damage and permit problems, Cost ~50% more than Vibroseis sources, can have difficult drill conditions, Variable source signature
Truck mounted vibrator coupled to land surface and a train of seismic waves over 3 – 6 seconds produced
To get a good seismic signal detonated in bedrock beneath the weathered layer.
  Quick and cheap (comparatively), As much energy as you want – simply add more trucks!, Source wavelet known
  Frequency content limited to 10 – 80 Hz, A lot of land needs to be cleared, only used on relatively flat ground

## Slide 17
Low frequency sources:
Airguns – penetrate up to 15 km (if air gun array)
Waterguns – up to a few km
High frequency sources:
Sparkers – up to around 2 km
Boomers – around 1 km
Chirp profiles – few 10’s m
Pingers – few m to couple of 10’s m
Depth of penetration will depend on properties
of the sediments
Marine sources

## Slide 18
Airguns (15 – 400 Hz)
From Kearey, Brooks and Hill, 2002.
Pneumatic source in which a chamber is filled from a compressor.
Rapid decompression of this chamber forms a large, expanding air bubble, which generates a pressure wave.

## Slide 19
http://www.youtube.com/watch?v=WpblB3xToZ4
Air gun bubble:
1. Air bubble from airgun expands until pressure of surrounding water overcomes its expansion, and forces it to contract
2. Bubble then collapses, compressing the air until the air pressure exceeds the water pressure, and the bubble can expand again
3. Expansion and collapse continues as bubble rises to surface, giving oscillatory signal characteristic of single airgun.
Single Airgun
7 Airguns
Source wavelet
Airguns (15 – 400 Hz)

## Slide 20
Aside: The ‘ideal’ wavelet
An ideal seismic source would be a spike and it would be repeatable
Provides the highest temporal resolution – no matter how closely spaced two reflectors are they could still be resolved
Maximum amplitude at every frequency
Time
Frequency
The “Minimum-phase” wavelet is the closest we can get to the ideal wavelet during seismic acquisition.
Minimum-phase wavelet has zero amplitude at t=0, and maximum amplitude a short time later
During acquisition a more ideal minimum-phase wavelet can be produced by air-gun tuning
Amplitude

## Slide 21
Aside: The ‘ideal’ wavelet
For interpretation purposes it would be more useful if the maximum energy of the
wavelet occurred at t=0, so a reflection from a horizon would be represented by a
peak or a trough rather than a point of zero amplitude.
The Ricker wavelet is “zero-phase”, it’s max amplitude occurs at t=0. It is impossible to create during acquisition, but we can convert a minimum-phase input wavelet into a Ricker wavelet during seismic processing
A Wiener filter is a filter designed to shape a wavelet (e.g. Minimum-phase) into another wavelet (eg. Zero-phase). Requires that the source wavelet shape is known. This process is called DECONVOLUTION (reverse of convolution)
Dominant frequency
AMPLITUDE
SPECTRA
(Frequency domain)
Recommended reading:
Phase, polarity and the interpreter’s wavelet
Simm & White, First Break v20, 2002

## Slide 22
Airgun environmental considerations
Weir and Dolman 2007, Journal of
International Wildlife Law and Policy
Airguns have highest energy at relatively low frequencies of 10-200 Hz, this overlaps with the frequency of sound produced by whales in particular
There is concern of the impact of airguns on marine mammals including 1) physical injury (e.g. hearing loss), 2) stress, 3) masking echolocation signals and having behavioral impacts
Airgun surveys employ a range of mitigation measures including 1) “ramping up” the airgun arrays, 2) having marine mammal observers to locate mammals and stop airguns, 3) design of surveys to avoid particular areas/times
http://cms.iucn.org

## Slide 23
http://www.pge.com
http://www.ga.gov.au/about/projects/marine/marine-seismic-surveys-and-the-environment
Airgun environmental considerations

## Slide 24
Sparkers (0.1 – 2.0 kHz)
Comprises many electrodes mounted on a single frame.
By discharging across these electrode we vaporize the surrounding sea water, producing a rapidly expanding plasma bubble.
Similar to airguns this produces our sound source.

## Slide 25
Pinger (commonly 3.5 kHz)
Generate the acoustic source by passing electrical energy through a piezoelectric crystal.
This causes the crystal to physically deform and thereby generate pressure wave.
Crystal acts as a transceiver, i.e., receives reflected energy as well.
Piezoelectricity (also called the piezoelectric effect) is the appearance of an electrical potential (a voltage, in other words) across the sides of a crystal when you subject it to mechanical stress (by squeezing it).

## Slide 26
Marine source data comparison
Airgun
Sparker
Pinger
~ 1.25 km
~150 m
~17 m

## Slide 27
Land receivers- Geophones
A geophone converts seismic energy (vibrations) into electrical voltage
which can be accurately measured
Geophones are fixed by a spike in soft ground or mounted firmly on hard
ground
The geophone moves with the ground during the passage of a seismic wave.
There is relative motion between a suspended coil and a magnet attached to
the geophone outer body, which generates a voltage across the terminals
http://www.linearcollider.org/newsline/images/2007

## Slide 28
Marine receivers - Hydrophones
Recommended reading:
A historical reflection on reflections,
Dragoset, Leading Edge, v24, 2005
Dragoset et al. 2005
Piezoelectric crystals

## Slide 29
The future? - Ocean Bottom Seismic
Ocean bottom cables (OBC)

## Slide 30
Learning outcomes
By the end of this lecture your should:
Understand why we need to use common depth point profiling methods to collect high-quality seismic data
2) Appreciate what sources are available and in what situation you would use different types of source
Thanks to: Yanghua Wang, Jenny Collier, Lidia Lonergan, Jo Morgan from Imperial College London, Chris Jackson from
the University of Manchester and Mark Vardy from SAND Geophysics for contributing material for this lecture series